## Slide 1
Institute for Modelling Hydraulic and Environmental Systems
Department of Hydromechanics and Modelling of Hydrosystems
FluidFlower Benchmark:
Participants Update 2
Bernd Flemisch
23.03.2022

## Slide 2: Third Submission 20.03.2022

## Slide 3: Reported Results Map of Phase Compositions
To be reported for each 24 hours after injection starts on a uniform Cartesian grid of 286 by 123 cells. For each temporal snapshot indicated by X hours, X = 24, 48, …, cell values should be provided in csv format in a file spatial_map_<X>h.csv of the form
# x, y, saturation [-], concentration [kg/m3] 5.000e-03, 5.000e-03, 1.234e+56, 1.234e+56 1.500e-02, 5.000e-03, 1.234e+56, 1.234e+56 … 2.855e+00, 5.000e-03, 1.234e+56, 1.234e+56 5.000e-03, 1.500e-02, 1.234e+56, 1.234e+56 1.500e-02, 1.500e-02, 1.234e+56, 1.234e+56 … … 2.845e+00, 1.225e+00, 1.234e+56, 1.234e+56 2.855e+00, 1.225e+00, 1.234e+56, 1.234e+56
The origin of the coordinate system should be located in the lower left corner with the x-axis positively oriented towards the right and the y-axis positively oriented towards the top.

## Slide 4: Spatial Maps: Saturation at t = 24 h

## Slide 5: Spatial Maps: Saturation at t = 48 h

## Slide 6: Spatial Maps: Saturation at t = 72 h

## Slide 7: Spatial Maps: Saturation at t = 96 h

## Slide 8: Spatial Maps: Saturation at t = 120 h

## Slide 9: Spatial Maps: Concentration at t = 24 h

## Slide 10: Spatial Maps: Concentration at t = 48 h

## Slide 11: Spatial Maps: Concentration at t = 72 h

## Slide 12: Spatial Maps: Concentration at t = 96 h

## Slide 13: Spatial Maps: Concentration at t = 120 h

## Slide 14: Reported Results Dense Data Time Series
All measurables identified in section 2.7 shall be reported at 10-minute intervals starting at the initial injection and lasting 120 hours. The data is expected in csv format in a file time_series.csv of the form
# t, p_1, …, totalCO2Mass 0.000e+00, 1.234e+56, 1.234e+56, <…> 6.000e+02, 1.234e+56, 1.234e+56, <…> ...
according to the measurables defined in section 2.7.

## Slide 15: Time Series: Total CO2 Mass

## Slide 16: Time Series: Pressure

## Slide 17: Time Series: Pressure Zoom into Time

## Slide 18: Time Series: Box A

## Slide 19: Time Series: Box B

## Slide 20: Time Series: Box C

## Slide 21: Reported Results Sparse Data Determination
Each of the sparse data shall be reported as six numbers:
  Prediction of the mean quantity as obtained by the experiments
  Prediction in the standard deviation of the quantity over the ensemble of experiments
  Stated in terms of P10, P50 and P90 values
Mean values assess the capability of predicting the various measurables
Standard deviations address the extent to which these quantities are deterministic
Any preferred methodology may be chosen:
  ensemble runs
  methods from uncertainty quantification
  human intuition from experience

## Slide 22: Reported Results Sparse Data Format
The quantities are expected to be uploaded to the repository in form of a csv file sparse_data.csv of the form
# idx, p10_mean, p50_mean, p90_mean, p10_dev, p50_dev, p90_dev 1a, 1.234e+56, <…>, # pressure at sensor 1 [N/m2] 1b, 1.234e+56, <…>, # pressure at sensor 2 [N/m2] 2, 1.234e+56, <…>, # time of max mobile free phase in Box A [s] 3a, 1.234e+56, <…>, # mobile free phase in Box A at 72h [kg/m2] 3b, 1.234e+56, <…>, # immobile free phase in Box A at 72h [kg/m2] 3c, 1.234e+56, <…>, # dissolved in water in Box A at 72h [kg/m2] 3d, 1.234e+56, <…>, # seal in Box A at 72h [kg/m2] 4a-d <same for Box B> 5, 1.234e+56, <…>, # time when M exceeds 110% of Box C’s width [s] 6, 1.234e+56, <…>, # total mass of CO2 in the top seal facies [kg]

## Slide 23: Sparse Data: Pressure

## Slide 24: Sparse Data: Time

## Slide 25: Sparse Data: CO2 in Box A at 72 h

## Slide 26: Sparse Data: CO2 in Box B at 72 h

## Slide 27: Modeling Choices, Discretization and Performance
Type | CSIRO | Delft-DARSim | Herriot-Watt | Imperial | LANL | Stanford | Stuttgart
Solubility limit [kg/m3] | 1.786 | 1.649 | 2.0 | 1.504 |  |  | 
Temperature [°C] | 20.0 | 20.0 | 20.0 | 20.0 |  |  | 
Domain volume [m3] | 0.0865 | 0.083 | 0.084 | 0.0875 |  |  | 
Cells | 44,284 | 43,758 | 42,000 | 4,437 – 30,784 | 24,748 | 6,094 / 21,392 | 26,099
Avg. Δt [s] | 1.96 / 35.9 | 13.1 / 79.8 | 100.0 | 0.16 | 6.0 | 2.28 | 20.44
Avg. nonlin. it. per time step | 3.0 / 3.0 | 1.3 / 1.0 | 10.0 | 9.9 | 1.0 | 1.07 | 7.3
Avg. linear it. per solve | - | - | - |  | - | - | -

## Slide 28: What‘s next?
Registration for final workshop: https://forms.gle/bWewqTn52iTMgQ3eA
Try to deliver all of the requested data, particularly the sparse data, or provide reasons why you don‘t, before 22.04.2022 23:59 h CET.

## Slide 29
Institut für Wasser- und Umweltsystemmodellierung Lehrstuhl für Hydromechanik und Hydrosystemmodellierung
Bernd Flemisch
E-Mail
bernd@iws.uni-stuttgart.de
Telefon +49 (0) 711 685-
69162
www.
iws.uni-stuttgart.de/lh2
Universität Stuttgart
IWS-LH2
Pfaffenwaldring 61, 70569 Stuttgart